## Slide 1: Introduction to Sockets Programming in C using TCP/IP

## Slide 2: Introduction
Computer Network
  hosts, routers,
communication channels
Hosts run applications
Routers forward information
Packets: sequence of bytes
  contain control information
  e.g. destination host
Protocol is an agreement
  meaning of packets
  structure and size of packets
e.g. Hypertext Transfer Protocol (HTTP)
Host
Router
Communication
channel

## Slide 3: Protocol Families - TCP/IP
Several protocols for different problems
Protocol Suites or Protocol Families: TCP/IP
TCP/IP provides end-to-end connectivity specifying how data should be
  formatted,
  addressed,
  transmitted,
  routed, and
  received at the destination
can be used in the internet and in stand-alone private networks
it is organized into layers

## Slide 4: TCP/IP
* image is taken from “http://en.wikipedia.org/wiki/TCP/IP_model”
*
FTP, SMTP, …
Transport Layer TCP or UDP
Network Layer IP
Communication Channels

## Slide 5: Internet Protocol (IP)
provides a datagram service
  packets are handled and delivered independently
best-effort protocol
  may loose, reorder or duplicate packets
each packet must contain an IP address of its destination

## Slide 6: Addresses - IPv4
Class A:
7
0 Network ID
24
Host ID
14
Class B:
1 0
Network ID
16
Host ID
Class C: | 1 | 1 | 0 |  | 21 Network ID |  | 8 Host ID
 |  |  |  |  |  | 28 | 
Class D (multicast): | 1 | 1 | 1 | 0 | Multicast | address | 
27
Class E (reserved):
unused
1 1 1 1 0
1.0.0.0 to 127.255.255.255
128.0.0.0 to 191.255.255.255
192.0.0.0 to 223.255.255.255
224.0.0.0 to 239.255.255.255
240.0.0.0 to 255.255.255.255
Range of addresses
The 32 bits of an IPv4 address are broken into 4 octets, or 8 bit fields (0-255 value in decimal notation).
For networks of different size,
  the first one (for large networks) to three (for small networks) octets can be used to identify the network, while
  the rest of the octets can be used to identify the node on the network.

## Slide 7: Local Area Network Addresses - IPv4

## Slide 8: TCP vs UDP
Both use port numbers
  application-specific construct serving as a communication endpoint
  16-bit unsigned integer, thus ranging from 0 to 65535
 to provide end-to-end transport
UDP: User Datagram Protocol
  no acknowledgements
  no retransmissions
  out of order, duplicates possible
  connectionless, i.e., app indicates destination for each packet
TCP: Transmission Control Protocol
  reliable byte-stream channel (in order, all arrive, no duplicates)
    similar to file I/O
  flow control
  connection-oriented
  bidirectional

## Slide 9: TCP vs UDP
TCP is used for services with a large data capacity, and a persistent connection
UDP is more commonly used for quick lookups, and single use query-reply actions.
Some common examples of TCP and UDP with their default ports:
DNS lookup | UDP | 53
FTP | TCP | 21
HTTP | TCP | 80
POP3 | TCP | 110
Telnet | TCP | 23

## Slide 10: Berkley Sockets
Universally known as Sockets
It is an abstraction through which an application may send and receive data
Provide generic access to interprocess communication services
  e.g. IPX/SPX, Appletalk, TCP/IP
Standard API for networking
Host
Application
Socket
TCP
IP
Host
Application
Socket
TCP
IP
Router
IP
Channel
Channel

## Slide 11: Sockets
Uniquely identified by
  an internet address
  an end-to-end protocol (e.g. TCP or UDP)
  a port number
Two types of (TCP/IP) sockets
  Stream sockets (e.g. uses TCP)
    provide reliable byte-stream service
  Datagram sockets (e.g. uses UDP)
    provide best-effort datagram service
    messages up to 65.500 bytes
Socket extend the convectional UNIX I/O facilities
  file descriptors for network communication
  extended the read and write system calls
0
1
2
internal data structure for file 1
Family: PF_INET
Service: SOCK_STREAM
Local_IP:
Remote_IP:
Local_Port:
Remote_Port:
…
Descriptor Table

## Slide 12: Sockets
TCP
UDP
IP
1 2
65535
1 2
Applications
TCP sockets
UDP sockets
TCP ports
65535 UDP ports
Descriptor references
Sockets bound to ports

## Slide 13: Socket Programming

## Slide 14: Client-Server communication
Server
  passively waits for and responds to clients
  passive socket
Client
  initiates the communication
  must know the address and the port of the server
  active socket

## Slide 15: Sockets - Procedures

## Slide 16: Client - Server Communication - Unix
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
socket()
connect()
send()
recv()
close()
Client
synchronization point
Stream (e.g. TCP)
socket()
bind()
recvfrom()
sendto()
close()
Server
socket()
sendto()
recvfrom()
close()
Client
Datagram (e.g. UDP)
bind()

## Slide 17: Socket creation in C: socket()
int sockid = socket(family, type, protocol);
  sockid: socket descriptor, an integer (like a file-handle)
  family: integer, communication domain, e.g.,
    PF_INET, IPv4 protocols, Internet addresses (typically used)
    PF_UNIX, Local communication, File addresses
  type: communication type
    SOCK_STREAM - reliable, 2-way, connection-based service
    SOCK_DGRAM - unreliable, connectionless, messages of maximum length
  protocol: specifies protocol
    IPPROTO_TCP IPPROTO_UDP
    usually set to 0 (i.e., use default protocol)
  upon failure returns -1
NOTE: socket call does not specify where data will be coming fr rom, nor where it will be going to – it just creates the interface!

## Slide 18: Client - Server Communication - Unix
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
socket()
connect()
send()
recv()
close()
Client
synchronization point
Stream (e.g. TCP)
socket()
bind()
recvfrom()
sendto()
close()
Server
socket()
sendto()
recvfrom()
close()
Client
Datagram (e.g. UDP)
bind()

## Slide 19: Socket close in C: close()
When finished using a socket, the socket should be closed
status = close(sockid);
  sockid: the file descriptor (socket being closed)
  status: 0 if successful, -1 if error
Closing a socket
  closes a connection (for stream socket)
  frees up the port used by the socket

## Slide 20: Specifying Addresses
Socket API defines a generic data type for addresses:
struct sockaddr {
unsigned short sa_family; /* Address family (e.g. AF_INET) */
char sa_data[14]; /* Family-specific address information */
}
Particular form of the sockaddr used for TCP/IP addresses:
struct in_addr {
unsigned long s_addr; /* Internet address (32 bits) */
}
Important: sockaddr_in can be casted to a sockaddr
}
struct sockaddr_in {
unsigned short sin_family; unsigned short sin_port; struct in_addr sin_addr; char sin_zero[8];
/* Internet protocol (AF_INET) */
/* Address port (16 bits) */
/* Internet address (32 bits) */
/* Not used */

## Slide 21: Client - Server Communication - Unix
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
socket()
connect()
send()
recv()
close()
Client
synchronization point
Stream (e.g. TCP)
socket()
bind()
recvfrom()
sendto()
close()
Server
socket()
sendto()
recvfrom()
close()
Client
Datagram (e.g. UDP)
bind()

## Slide 22: Assign address to socket: bind()
associates and reserves a port for use by the socket
int status = bind(sockid, &addrport, size);
  sockid: integer, socket descriptor
  addrport: struct sockaddr, the (IP) address and port of the machine
    for TCP/IP server, internet address is usually set to INADDR_ANY, i.e., chooses any incoming interface
  size: the size (in bytes) of the addrport structure
  status: upon failure -1 is returned

## Slide 23: bind()- Example with TCP
int sockid;
struct sockaddr_in addrport;
sockid = socket(PF_INET, SOCK_STREAM, 0);
addrport.sin_family = AF_INET; addrport.sin_port = htons(5100); addrport.sin_addr.s_addr = htonl(INADDR_ANY);
if(bind(sockid, (struct sockaddr *) &addrport, sizeof(addrport))!= -1) {
…}

## Slide 24: Skipping the bind()
bind can be skipped for both types of sockets
Datagram socket:
  if only sending, no need to bind. The OS finds a port each time the socket sends a packet
  if receiving, need to bind
Stream socket:
  destination determined during connection setup
  don’t need to know port sending from (during connection setup, receiving end is informed of port)

## Slide 25: Client - Server Communication - Unix
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
socket()
connect()
send()
recv()
close()
Client
synchronization point
Stream (e.g. TCP)
socket()
bind()
recvfrom()
sendto()
close()
Server
socket()
sendto()
recvfrom()
close()
Client
Datagram (e.g. UDP)
bind()

## Slide 26: Assign address to socket: bind()
Instructs TCP protocol implementation to listen for connections
int status = listen(sockid, queueLimit);
  sockid: integer, socket descriptor
  queuelen: integer, # of active participants that can “wait” for a connection
  status: 0 if listening, -1 if error
listen() is non-blocking: returns immediately
The listening socket (sockid)
  is never used for sending and receiving
  is used by the server only as a way to get new sockets

## Slide 27: Client - Server Communication - Unix
socket()
bind()
accept()
recv()
send()
close()
Server
socket()
connect()
send()
recv()
close()
Client
listen()
synchronization
point
Stream (e.g. TCP)
socket()
bind()
recvfrom()
sendto()
close()
Server
socket()
sendto()
recvfrom()
close()
Client
Datagram (e.g. UDP)
bind()

## Slide 28: Establish Connection: connect()
The client establishes a connection with the server by calling
connect()
int status = connect(sockid, &foreignAddr, addrlen);
  sockid: integer, socket to be used in connection
  foreignAddr: struct sockaddr: address of the passive participant
  addrlen: integer, sizeof(name)
  status: 0 if successful connect, -1 otherwise
connect() is blocking

## Slide 29: Incoming Connection: accept()
The server gets a socket for an incoming client connection by calling
accept()
int s = accept(sockid, &clientAddr, &addrLen);
  s: integer, the new socket (used for data-transfer)
  sockid: integer, the orig. socket (being listened on)
  clientAddr: struct sockaddr, address of the active participant
    filled in upon return
  addrLen: sizeof(clientAddr): value/result parameter
    must be set appropriately before call
    adjusted upon return
accept()
  is blocking: waits for connection before returning
  dequeues the next connection on the queue for socket (sockid)

## Slide 30: Client - Server Communication - Unix
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
socket()
connect()
send()
recv()
close()
Client
synchronization point
Stream (e.g. TCP)
socket()
bind()
recvfrom()
sendto()
close()
Server
socket()
sendto()
recvfrom()
close()
Client
Datagram (e.g. UDP)
bind()

## Slide 31: Exchanging data with stream socket
int count = send(sockid, msg, msgLen, flags);
  msg: const void[], message to be transmitted
  msgLen: integer, length of message (in bytes) to transmit
  flags: integer, special options, usually just 0
  count: # bytes transmitted (-1 if error)
int count = recv(sockid, recvBuf, bufLen, flags);
  recvBuf: void[], stores received bytes
  bufLen: # bytes received
  flags: integer, special options, usually just 0
  count: # bytes received (-1 if error)
Calls are blocking
 returns only after data is sent / received

## Slide 32: Exchanging data with datagram socket
int count = sendto(sockid, msg, msgLen, flags, &foreignAddr, addrlen);
  msg, msgLen, flags, count: same with send()
  foreignAddr: struct sockaddr, address of the destination
  addrLen: sizeof(foreignAddr)
int count = recvfrom(sockid, recvBuf, bufLen, flags, &clientAddr, addrlen);
  recvBuf, bufLen, flags, count: same with recv()
  clientAddr: struct sockaddr, address of the client
  addrLen: sizeof(clientAddr)
Calls are blocking
  returns only after data is sent / received

## Slide 33: Example - Echo
A client communicates with an “echo” server
The server simply echoes whatever it receives back to the client

## Slide 34: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
The server starts by getting ready to receive client connections…

## Slide 35: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
/* Create socket for incoming connections */
if ((servSock = socket(PF_INET, SOCK_STREAM, IPPROTO_TCP)) < 0) DieWithError("socket() failed");

## Slide 36: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
echoServAddr.sin_family = AF_INET; /* Internet address family */ echoServAddr.sin_addr.s_addr = htonl(INADDR_ANY); /* Any incoming interface */ echoServAddr.sin_port = htons(echoServPort); /* Local port */
if (bind(servSock, (struct sockaddr *) &echoServAddr, sizeof(echoServAddr)) < 0) DieWithError("bind() failed");

## Slide 37: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
/* Mark the socket so it will listen for incoming connections */
if (listen(servSock, MAXPENDING) < 0) DieWithError("listen() failed");

## Slide 38: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
for (;;) /* Run forever */
{
clntLen = sizeof(echoClntAddr);
if ((clientSock=accept(servSock,(struct sockaddr *)&echoClntAddr,&clntLen))<0) DieWithError("accept() failed");
...

## Slide 39: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
Server is now blocked waiting for connection from a client
…
A client decides to talk to the server

## Slide 40: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
/* Create a reliable, stream socket using TCP */
if ((clientSock = socket(PF_INET, SOCK_STREAM, IPPROTO_TCP)) < 0) DieWithError("socket() failed");

## Slide 41: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
echoServAddr.sin_family = AF_INET; /* Internet address family */ echoServAddr.sin_addr.s_addr = inet_addr(echoservIP); /* Server IP address*/ echoServAddr.sin_port = htons(echoServPort); /* Server port */
if (connect(clientSock, (struct sockaddr *) &echoServAddr,
sizeof(echoServAddr)) < 0) DieWithError("connect() failed");

## Slide 42: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
for (;;) /* Run forever */
{
clntLen = sizeof(echoClntAddr);
if ((clientSock=accept(servSock,(struct sockaddr *)&echoClntAddr,&clntLen))<0) DieWithError("accept() failed");
...
Server’s accept procedure in now unblocked and returns client’s socket

## Slide 43: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
echoStringLen = strlen(echoString); /* Determine input length */
/* Send the string to the server */
if (send(clientSock, echoString, echoStringLen, 0) != echoStringLen) DieWithError("send() sent a different number of bytes than expected");

## Slide 44: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
/* Receive message from client */
if ((recvMsgSize = recv(clntSocket, echoBuffer, RCVBUFSIZE, 0)) < 0) DieWithError("recv() failed");
/* Send received string and receive again until end of transmission */
while (recvMsgSize > 0) { /* zero indicates end of transmission */
if (send(clientSocket, echobuffer, recvMsgSize, 0) != recvMsgSize) DieWithError(“send() failed”);
if ((recvMsgSize = recv(clientSocket, echoBuffer, RECVBUFSIZE, 0)) < 0) DieWithError(“recv() failed”);
}

## Slide 45: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
Similarly, the client receives the data from the server

## Slide 46: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
  Accept new connection
  Communicate
  Close the connection
close(clientSock);
close(clientSock);

## Slide 47: Example - Echo using stream socket
Client
Create a TCP socket
Establish connection
Communicate
Close the connection
Server
Create a TCP socket
Assign a port to socket
Set socket to listen
Repeatedly:
Accept new connection
Communicate
Close the connection
Server is now blocked waiting for connection from a client
…

## Slide 48: Example - Echo using datagram socket
Client
Create a UDP socket
Assign a port to socket
Communicate
Close the socket

Server
Create a UDP socket
Assign a port to socket
Repeatedly
Communicate
/* Create socket for sending/receiving datagrams */
if ((servSock = socket(PF_INET, SOCK_DGRAM, IPPROTO_UDP)) < 0) DieWithError("socket() failed");
/* Create a datagram/UDP socket */
if ((clientSock = socket(PF_INET, SOCK_DGRAM, IPPROTO_UDP)) < 0) DieWithError("socket() failed");

## Slide 49: Example - Echo using datagram socket
Client
Create a UDP socket
Assign a port to socket
Communicate
Close the socket

Server
Create a UDP socket
Assign a port to socket
Repeatedly
Communicate
echoServAddr.sin_family = AF_INET; /* Internet address family */ echoServAddr.sin_addr.s_addr = htonl(INADDR_ANY); /* Any incoming interface */ echoServAddr.sin_port = htons(echoServPort); /* Local port */
if (bind(servSock, (struct sockaddr *) &echoServAddr, sizeof(echoServAddr)) < 0) DieWithError("bind() failed");
echoClientAddr.sin_family = AF_INET; /* Internet address family */ echoClientAddr.sin_addr.s_addr = htonl(INADDR_ANY); /* Any incoming interface */ echoClientAddr.sin_port = htons(echoClientPort); /* Local port */
if(bind(clientSock,(struct sockaddr *)&echoClientAddr,sizeof(echoClientAddr))<0) DieWithError("connect() failed");

## Slide 50: Example - Echo using datagram socket
Client
Create a UDP socket
Assign a port to socket
Communicate
Close the socket

Server
Create a UDP socket
Assign a port to socket
Repeatedly
Communicate
echoServAddr.sin_family = AF_INET; echoServAddr.sin_addr.s_addr = inet_addr(echoservIP); echoServAddr.sin_port = htons(echoServPort);
/* Internet address family */
/* Server IP address*/
/* Server port */
echoStringLen = strlen(echoString); /* Determine input length */
/* Send the string to the server */
if (sendto( clientSock, echoString, echoStringLen, 0,
(struct sockaddr *) &echoServAddr, sizeof(echoServAddr))
!= echoStringLen)
DieWithError("send() sent a different number of bytes than expected");

## Slide 51: Example - Echo using datagram socket
Client
Create a UDP socket
Assign a port to socket
Communicate
Close the socket

Server
Create a UDP socket
Assign a port to socket
Repeatedly
Communicate
/* Set the size of the in-out parameter */
for (;;) /* Run forever */
{
clientAddrLen = sizeof(echoClientAddr)
/*Block until receive message from client*/
if ((recvMsgSize = recvfrom(servSock, echoBuffer, ECHOMAX, 0),
(struct sockaddr *) &echoClientAddr, sizeof(echoClientAddr))) < 0) DieWithError(“recvfrom() failed");
if (sendto(servSock, echobuffer, recvMsgSize, 0,
(struct sockaddr *) &echoClientAddr, sizeof(echoClientAddr))
!= recvMsgSize) DieWithError(“send() failed”);
}

## Slide 52: Example - Echo using datagram socket
Client
Create a UDP socket
Assign a port to socket
Communicate
Close the socket

Server
Create a UDP socket
Assign a port to socket
Repeatedly
Communicate
Similarly, the client receives the data from the server

## Slide 53: Example - Echo using datagram socket
close(clientSock);
Client
Create a UDP socket
Assign a port to socket
Communicate
Close the socket

Server
Create a UDP socket
Assign a port to socket
Repeatedly
Communicate

## Slide 54: Client - Server Communication - Unix
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
socket()
connect()
send()
recv()
close()
Client
synchronization point
Stream (e.g. TCP)
socket()
bind()
recvfrom()
sendto()
close()
Server
socket()
sendto()
recvfrom()
close()
Client
Datagram (e.g. UDP)
bind()

## Slide 55: Constructing Messages - Encoding Data
Client wants to send two integers x and y to server
1st Solution: Character Encoding
  e.g. ASCII
 the same representation is used to print or display them to screen
 allows sending arbitrarily large numbers (at least in principle)
e.g. x = 17,998,720 and y = 47,034,615
49 | 55 | 57 | 57 | 56 | 55 | 50 | 48 | 32 | 52 | 55 | 48 | 51 | 52 | 54 | 49 | 53 | 32
1
7
9
9
8
7
2
0
_
4
7
0
3
4
6
1
5
_
sprintf(msgBuffer, “%d %d ”, x, y); send(clientSocket, strlen(msgBuffer), 0);

## Slide 56: Constructing Messages - Encoding Data
Pitfalls
  the second delimiter is required
    otherwise the server will not be able to separate it from whatever it follows
  msgBuffer must be large enough
  strlen counts only the bytes of the message
    not the null at the end of the string
 This solution is not efficient
 each digit can be represented using 4 bits, instead of one byte
 it is inconvenient to manipulate numbers
2nd Solution: Sending the values of x and y

## Slide 57: Constructing Messages - Encoding Data
2nd Solution: Sending the values of x and y
  pitfall: native integer format
 a protocol is used
    how many bits are used for each integer
    what type of encoding is used (e.g. two’s complement, sign/magnitude, unsigned)
1st Implementation
typedef struct { int x,y;
} msgStruct;
…
msgStruct.x = x; msgStruct.y = y; send(clientSock, &msgStruct, sizeof(msgStruct), 0);
send(clientSock, &x, sizeof(x)), 0); send(clientSock, &y, sizeof(y)), 0);
2nd Implementation
2nd implementation works in any case?

## Slide 58: Constructing Messages - Byte Ordering
Address and port are stored as integers
  u_short sin_port; (16 bit)
  in_addr sin_addr; (32 bit)
Problem:
  different machines / OS’s use different word orderings
    little-endian: lower bytes first
    big-endian: higher bytes first
  these machines may communicate with one another over the network
128.119.40.12
128 | 119 | 40 | 12
12.40.119.128
128 | 119 | 40 | 12
Big-Endian
machine
Little-Endian machine

## Slide 59: Constructing Messages - Byte Ordering
Big-Endian:
Little-Endian:

## Slide 60: Constructing Messages - Byte Ordering -
Solution: Network Byte Ordering
Host Byte-Ordering: the byte ordering used by a host (big or little)
Network Byte-Ordering: the byte ordering used by the network – always big-endian
u_long htonl(u_long x);
u_short htons(u_short x);
u_long ntohl(u_long x);
u_short ntohs(u_short x);
On big-endian machines, these routines do nothing
On little-endian machines, they reverse the byte order
128
.119.4
0.12
128 | 119 | 40 | 12
0.12
.119.4
128
128 | 119 | 40 | 12
Big-Endia
machine
-Endian
ine
n Little mach
htonl
ntohl
128 | 119 | 40 | 12
128
119
40
12

## Slide 61: Constructing Messages - Byte Ordering -
unsigned short clientPort, message; unsigned int messageLenth;
servPort = 1111;
message = htons(clientPort); messageLength = sizeof(message);
if (sendto( clientSock, message, messageLength, 0,
(struct sockaddr *) &echoServAddr, sizeof(echoServAddr))
!= messageLength)
DieWithError("send() sent a different number of bytes than expected");
Server
Client
unsigned short clientPort, rcvBuffer; unsigned int recvMsgSize ;
if ( recvfrom(servSock, &rcvBuffer, sizeof(unsigned int), 0),
(struct sockaddr *) &echoClientAddr, sizeof(echoClientAddr)) < 0) DieWithError(“recvfrom() failed");
clientPort = ntohs(rcvBuffer);
printf (“Client’s port: %d”, clientPort);
Example

## Slide 62: Constructing Messages - Alignment and Padding
consider the following 12 byte structure
After compilation it will be a 14 byte structure!
Why? € Alignment!
Remember the following rules:
  data structures are maximally aligned, according to the size of the largest native integer
  other multibyte fields are aligned to their size, e.g., a four-byte integer’s address will be divisible by four
typedef struct { int x;
short x2; int y; short y2;
} msgStruct;
x | x2 | y | y2
4 bytes 2 bytes 4 bytes 2 bytes
This can be avoided
  include padding to data structure
  reorder fields
x | x2 | [pad] | y | y2
4 bytes 2 bytes 2 bytes 4 bytes 2 bytes
typedef struct { int x;
short x2; char pad[2]; int y;
short y2;
} msgStruct;
typedef struct { int x;
int y; short x2; short y2;
} msgStruct;

## Slide 63: Constructing Messages - Framing and Parsing
Framing is the problem of formatting the information so that the receiver can parse messages
Parse means to locate the beginning and the end of message
This is easy if the fields have fixed sizes
  e.g., msgStruct
For text-string representations is harder
  Solution: use of appropriate delimiters
  caution is needed since a call of recv may return the messages sent by multiple calls of send

## Slide 64: Socket Options
getsockopt and setsockopt allow socket options values to be queried and set, respectively
int getsockopt (sockid, level, optName, optVal, optLen);
  sockid: integer, socket descriptor
  level: integer, the layers of the protocol stack (socket, TCP, IP)
  optName: integer, option
  optVal: pointer to a buffer; upon return it contains the value of the specified option
  optLen: integer, in-out parameter it returns -1 if an error occured
int setsockopt (sockid, level, optName, optVal, optLen);
  optLen is now only an input parameter

## Slide 65: Socket Options - Table

## Slide 66: Socket Options - Example
66
Fetch and then double the current number of bytes in the socket’s receive buffer
int rcvBufferSize; int sockOptSize;
…
/* Retrieve and print the default buffer size */
sockOptSize = sizeof(recvBuffSize);
if (getsockopt(sock, SOL_SOCKET, SO_RCVBUF, &rcvBufferSize, &sockOptSize) < 0) DieWithError(“getsockopt() failed”);
printf(“Initial Receive Buffer Size: %d\n”, rcvBufferSize);
/* Double the buffer size */
recvBufferSize *= 2;
/* Set the buffer size to new value */
if (setsockopt(sock, SOL_SOCKET, SO_RCVBUF, &rcvBufferSize, sizeof(rcvBufferSize)) < 0)
DieWithError(“getsockopt() failed”);

## Slide 67: Dealing with blocking calls
67
Many of the functions we saw block (by default) until a certain event
  accept: until a connection comes in
  connect: until the connection is established
  recv, recvfrom: until a packet (of data) is received
    what if a packet is lost (in datagram socket)?
  send: until data are pushed into socket’s buffer
  sendto: until data are given to the network subsystem
For simple programs, blocking is convenient
What about more complex programs?
  multiple connections
  simultaneous sends and receives
  simultaneously doing non-networking processing

## Slide 68: Dealing with blocking calls
68
Non-blocking Sockets
Asynchronous I/O
Timeouts

## Slide 69: Non-blocking Sockets
69
If an operation can be completed immediately, success is returned; otherwise, a failure is returned (usually -1)
  errno is properly set, to distinguish this (blocking) failure from other - (EINPROGRESS for connect, EWOULDBLOCK for the other)
1st Solution: int fcntl (sockid, command, argument);
  sockid: integer, socket descriptor
  command: integer, the operation to be performed (F_GETFL, F_SETFL)
  argument: long, e.g. O_NONBLOCK
 fcntl (sockid, F_SETFL, O_NONBLOCK);
2nd Solution: flags parameter of send, recv, sendto, recvfrom
  MSG_DONTWAIT
  not supported by all implementations

## Slide 70: Signals
70
Provide a mechanism for operating system to notify processes that certain events occur
  e.g., the user typed the “interrupt” character, or a timer expired
signals are delivered asynchronously
upon signal delivery to program
  it may be ignored, the process is never aware of it
  the program is forcefully terminated by the OS
  a signal-handling routine, specified by the program, is executed
    this happens in a different thread
  the signal is blocked, until the program takes action to allow its delivery
    each process (or thread) has a corresponding mask
Each signal has a default behavior
  e.g. SIGINT (i.e., Ctrl+C) causes termination
  it can be changed using sigaction()
Signals can be nested (i.e., while one is being handled another is delivered)

## Slide 71: Signals
71
int sigaction(whichSignal, &newAction, &oldAction);
  whichSignal: integer
  newAction: struct sigaction, defines the new behavior
  oldAction: struct sigaction, if not NULL, then previous behavior is copied
  it returns 0 on success, -1 otherwise
struct sigaction {
void (*sa_handler)(int); /* Signal handler */
sigset_t sa_mask; /* Signals to be blocked during handler execution */ int sa_flags; /* Flags to modify default behavior */
};
sa_handler determines which of the first three possibilities occurs when signal is delivered, i.e., it is not masked
  SIG_IGN, SIG_DFL, address of a function
sa_mask specifies the signals to be blocked while handling whichSignal
  whichSignal is always blocked
  it is implemented as a set of boolean flags
int sigemptyset (sigset_t *set); /* unset all the flags */
int sigfullset (sigset_t *set); /* set all the flags */
int sigaddset(sigset_t *set, int whichSignal); /* set individual flag */
int sigdelset(sigset_t *set, int whichSignal); /* unset individual flag */

## Slide 72: Signals - Example
#include <stdio.h> #include <signal.h> #include <unistd.h>
void DieWithError(char *errorMessage);
void InterruptSignalHandler(int signalType);
72
/* Signal handler specification structure */
/* Set handler function */
/* Create mask that masks all signals */
/* Set signal handling for interrupt signals */
/* Suspend program until signal received */
int main (int argc, char *argv[]) {
struct sigaction handler;
handler.sa_handler = InterruptSignalHandler;
if (sigfillset(&handler.sa_mask) < 0) DieWithError (“sigfillset() failed”);
handler.sa_flags = 0;
if (sigaction(SIGINT, &handler, 0) < 0) DieWithError (“sigaction() failed”);
for(;;) pause(); exit(0);
}
void InterruptHandler (int signalType) {
printf (“Interrupt received. Exiting program.\n); exit(1);
}

## Slide 73: Asynchronous I/O
73
 Non-blocking sockets require “polling”
 With asynchronous I/O the operating system informs the program when a socket call is completed
the SIGIO signal is delivered to the process, when some I/O-related event occurs on the socket
Three steps:
/* i. inform the system of the desired disposition of the signal */ struct sigaction handler; handler.sa_handler = SIGIOHandler;
if (sigfillset(&handler.sa_mask) < 0) DiewithError(“…”); handler.sa_flags = 0;
if (sigaction(SIGIO, &handler, 0) < 0) DieWithError(“…”);
/* ii. ensure that signals related to the socket will be delivered to this process */
if (fcntl(sock, F_SETOWN, getpid()) < 0) DieWithError();
/* iii. mark the socket as being primed for asynchronous I/O */
if (fcntl(sock, F_SETFL, O_NONBLOCK | FASYNC) < 0) DieWithError();

## Slide 74: Timeouts
74
Using asynchronous I/O the operating system informs the program for the occurrence of an I/O related event
  what happens if a UPD packet is lost?
We may need to know if something doesn’t happen after some time
unsigned int alarm (unsigned int secs);
  starts a timer that expires after the specified number of seconds (secs)
  returns
    the number of seconds remaining until any previously scheduled alarm was due to be delivered,
    or zero if there was no previously scheduled alarm
  process receives SIGALARM signal when timer expires and errno is set to
EINTR

## Slide 75: Asynchronous I/O - Example
75
/* Inform the system of the desired disposition of the signal */ struct sigaction myAction; myAction.sa_handler = CatchAlarm;
if (sigfillset(&myAction.sa_mask) < 0) DiewithError(“…”); myAction.sa_flags = 0;
if (sigaction(SIGALARM, &handler, 0) < 0) DieWithError(“…”);
/* Set alarm */
alarm(TIMEOUT_SECS);
/* Call blocking receive */
if (recvfrom(sock, echoBuffer, ECHOMAX, 0, … ) < 0) { if (errno = EINTR) … /*Alarm went off */
else DieWithError(“recvfrom() failed”);
}

## Slide 76: Iterative Stream Socket Server
76
Handles one client at a time
Additional clients can connect while one is being served
  connections are established
  they are able to send requests
but, the server will respond after it finishes with the first client
 Works well if each client required a small, bounded amount of work by the server
 otherwise, the clients experience long delays

## Slide 77: Iterative Server - Example: echo using stream socket
#include <stdio.h> /* for printf() and fprintf() */
#include <sys/socket.h> /* for socket(), bind(), connect(), recv() and send() */
77
#include <arpa/inet.h> #include <stdlib.h> #include <string.h> #include <unistd.h>
/* for sockaddr_in and inet_ntoa() */
/* for atoi() and exit() */
/* for memset() */
/* for close() */
#define MAXPENDING 5 /* Maximum outstanding connection requests */
void DieWithError(char *errorMessage); /* Error handling function */
void HandleTCPClient(int clntSocket); /* TCP client handling function */
int main(int argc, char *argv[]) { int servSock;
int clntSock;
/* Socket descriptor for server */
/* Socket descriptor for client */
struct sockaddr_in echoServAddr; /* Local address */ struct sockaddr_in echoClntAddr; /* Client address */
unsigned short echoServPort; unsigned int clntLen;
/* Server port */
/* Length of client address data structure */
if (argc != 2) { /* Test for correct number of arguments */ fprintf(stderr, "Usage: %s <Server Port>\n", argv[0]); exit(1);
}
echoServPort = atoi(argv[1]); /* First arg: local port */
/* Create socket for incoming connections */
if ((servSock = socket(PF_INET, SOCK_STREAM, IPPROTO_TCP)) < 0) DieWithError("socket() failed");
...

## Slide 78: Iterative Server - Example: echo using stream socket
...
78
/* Construct local address structure */ memset(&echoServAddr, 0, sizeof(echoServAddr)); echoServAddr.sin_family = AF_INET;
/* Zero out structure */
/* Internet address family */
echoServAddr.sin_addr.s_addr = htonl(INADDR_ANY); /* Any incoming interface */
echoServAddr.sin_port = htons(echoServPort); /* Local port */
/* Bind to the local address */
if (bind(servSock, (struct sockaddr *) &echoServAddr, sizeof(echoServAddr)) < 0) DieWithError("bind() failed");
/* Mark the socket so it will listen for incoming connections */ if (listen(servSock, MAXPENDING) < 0)
DieWithError("listen() failed");
for (;;) /* Run forever */
{
/* Set the size of the in-out parameter */ clntLen = sizeof(echoClntAddr);
/* Wait for a client to connect */
if ((clntSock = accept(servSock, (struct sockaddr *) &echoClntAddr,
&clntLen)) < 0) DieWithError("accept() failed");
/* clntSock is connected to a client! */
printf("Handling client %s\n", inet_ntoa(echoClntAddr.sin_addr)); HandleTCPClient(clntSock);
}
/* NOT REACHED */
}

## Slide 79: Iterative Server - Example: echo using stream socket
#define RCVBUFSIZE 32 /* Size of receive buffer */
79
void HandleTCPClient(int clntSocket)
{
char echoBuffer[RCVBUFSIZE]; int recvMsgSize;
/* Buffer for echo string */
/* Size of received message */
/* Receive message from client */
if ((recvMsgSize = recv(clntSocket, echoBuffer, RCVBUFSIZE, 0)) < 0) DieWithError("recv() failed");
/* Send received string and receive again until end of transmission */ while (recvMsgSize > 0) /* zero indicates end of transmission */
{
/* Echo message back to client */
if (send(clntSocket, echoBuffer, recvMsgSize, 0) != recvMsgSize) DieWithError("send() failed");
/* See if there is more data to receive */
if ((recvMsgSize = recv(clntSocket, echoBuffer, RCVBUFSIZE, 0)) < 0) DieWithError("recv() failed");
}
close(clntSocket); /* Close client socket */
}

## Slide 80: Multitasking - Per-Client Process
80
For each client connection request, a new process is created to handle the communication
int fork();
  a new process is created, identical to the calling process, except for its process ID and the return value it receives from fork()
  returns 0 to child process, and the process ID of the new child to parent
Caution:
  when a child process terminates, it does not automatically disappears
  use waitpid() to parent in order to “harvest” zombies

## Slide 81: Multitasking - Per-Client Process
- Example: echo using stream socket
#include <sys/wait.h> /* for waitpid() */
81
int main(int argc, char *argv[]) { int servSock;
int clntSock;
unsigned short echoServPort;
pid_t processID;
unsigned int childProcCount = 0;
/* Socket descriptor for server */
/* Socket descriptor for client */
/* Server port */
/* Process ID from fork()*/
/* Number of child processes */
if (argc != 2) { /* Test for correct number of arguments */ fprintf(stderr, "Usage: %s <Server Port>\n", argv[0]); exit(1);
}
echoServPort = atoi(argv[1]); /* First arg: local port */
servSock = CreateTCPServerSocket(echoServPort); for (;;) { /* Run forever */
clntSock = AcceptTCPConnection(servSock);
if ((processID = fork()) < 0) DieWithError (“fork() failed”); /* Fork child process */
/* This is the child process */
/* child closes listening socket */
/* child process terminates */
else if (processID = 0) { close(servSock); HandleTCPClient(clntSock); exit(0);
}
close(clntSock); childProcCount++;
/* parent closes child socket */
/* Increment number of outstanding child processes */
...

## Slide 82: Multitasking - Per-Client Process - Example: echo using stream socket
/* Clean up all zombies */
/* Non-blocking wait */
/* No zombie to wait */
/* Cleaned up after a child */
82
...
while (childProcCount) {
processID = waitpid((pid_t) -1, NULL, WHOANG); if (processID < 0) DieWithError (“...”);
else if (processID == 0) break; else childProcCount--;
}
}
/* NOT REACHED */
}

## Slide 83: Multitasking - Per-Client Thread
83
 Forking a new process is expensive
duplicate the entire state (memory, stack, file/socket descriptors, …)
 Threads decrease this cost by allowing multitasking within the same process
threads share the same address space (code and data)
An example is provided using POSIX Threads

## Slide 84: Multitasking - Per-Client Thread
- Example: echo using stream socket
#include <pthread.h>
84
/* for POSIX threads */
void *ThreadMain(void *arg)
/* Main program of a thread */
/* Structure of arguments to pass to client thread */
/* socket descriptor for client */
struct ThreadArgs { int clntSock;
};
int main(int argc, char *argv[]) { int servSock;
int clntSock;
unsigned short echoServPort;
pthread_t threadID;
struct ThreadArgs *threadArgs;
/* Socket descriptor for server */
/* Socket descriptor for client */
/* Server port */
/* Thread ID from pthread_create()*/
/* Pointer to argument structure for thread */
if (argc != 2) { /* Test for correct number of arguments */ fprintf(stderr, "Usage: %s <Server Port>\n", argv[0]); exit(1);
}
echoServPort = atoi(argv[1]); /* First arg: local port */
servSock = CreateTCPServerSocket(echoServPort); for (;;) { /* Run forever */
clntSock = AcceptTCPConnection(servSock);
/* Create separate memory for client argument */
if ((threadArgs = (struct ThreadArgs *) malloc(sizeof(struct ThreadArgs)))) == NULL) DieWithError(“…”);
threadArgs -> clntSock = clntSock;
/* Create client thread */
if (pthread_create (&threadID, NULL, ThreadMain, (void *) threadArgs) != 0) DieWithError(“…”);
}
/* NOT REACHED */
}

## Slide 85: Multitasking - Per-Client Thread
85
- Example: echo using stream socket
void *ThreadMain(void *threadArgs)
{
int clntSock; /* Socket descriptor for client connection */
pthread_detach(pthread_self()); /* Guarantees that thread resources are deallocated upon return */
/* Extract socket file descriptor from argument */
clntSock = ((struct ThreadArgs *) threadArgs) -> clntSock; free(threadArgs); /* Deallocate memory for argument */
HandleTCPClient(clntSock); return (NULL);
}

## Slide 86: Multitasking - Constrained
86
Both process and thread incurs overhead
  creation, scheduling and context switching
As their numbers increases
  this overhead increases
  after some point it would be better if a client was blocked
Solution: Constrained multitasking. The server:
  begins, creating, binding and listening to a socket
  creates a number of processes, each loops forever and accept connections from the same socket
  when a connection is established
    the client socket descriptor is returned to only one process
    the other remain blocked

## Slide 87: Multitasking - Constrained
- Example: echo using stream socket
void ProcessMain(int servSock); /* Main program of process */
87
int main(int argc, char *argv[]) { int servSock;
unsigned short echoServPort; pid_t processID;
unsigned int processLimit; unsigned int processCt;
/* Socket descriptor for server*/
/* Server port */
/* Process ID */
/* Number of child processes to create */
/* Process counter */
if (argc != 3) { /* Test for correct number of arguments */ fprintf(stderr,"Usage: %s <SERVER PORT> <FORK LIMIT>\n", argv[0]); exit(1);
}
echoServPort = atoi(argv[1]); /* First arg: local port */
processLimit = atoi(argv[2]); /* Second arg: number of child processes */
servSock = CreateTCPServerSocket(echoServPort);
for (processCt=0; processCt < processLimit; processCt++)
if ((processID = fork()) < 0) DieWithError("fork() failed"); else if (processID == 0) ProcessMain(servSock);
/* Fork child process */
/* If this is the child process */
exit(0); /* The children will carry on */
}
void ProcessMain(int servSock) {
int clntSock; /* Socket descriptor for client connection */
for (;;) { /* Run forever */
clntSock = AcceptTCPConnection(servSock);
printf("with child process: %d\n", (unsigned int) getpid()); HandleTCPClient(clntSock);
}
}

## Slide 88: Multiplexing
88
So far, we have dealt with a single I/O channel
We may need to cope with multiple I/O channels
  e.g., supporting the echo service over multiple ports
Problem: from which socket the server should accept connections or receive messages?
  it can be solved using non-blocking sockets
 but it requires polling
Solution: select()
  specifies a list of descriptors to check for pending I/O operations
  blocks until one of the descriptors is ready
  returns which descriptors are ready

## Slide 89: Multiplexing
int select (maxDescPlus1, &readDescs, &writeDescs, &exceptionDescs, &timeout);
  maxDescsPlus1: integer, hint of the maximum number of descriptors
  readDescs: fd_set, checked for immediate input availability
  writeDescs: fd_set, checked for the ability to immediately write data
  exceptionDescs: fd_set, checked for pending exceptions
  timeout: struct timeval, how long it blocks (NULL € forever)
returns the total number of ready descriptors, -1 in case of error
changes the descriptor lists so that only the corresponding positions are set
int FD_ZERO (fd_set *descriptorVector);
int FD_CLR (int descriptor, fd_set *descriptorVector); int FD_SET (int descriptor, fd_set *descriptorVector);
89
int FD_ISSET (int descriptor, fd_set *descriptorVector);
/* removes all descriptors from vector */
/* remove descriptor from vector */
/* add descriptor to vector */
/* vector membership check */
struct timeval {
time_t tv_sec; /* seconds */ time_t tv_usec; /* microseconds */
};

## Slide 90: Multiplexing - Example: echo using stream socket
#include <sys/time.h> /* for struct timeval {} */
90
int main(int argc, char *argv[])
{
int *servSock;
int maxDescriptor; fd_set sockSet; long timeout;
struct timeval selTimeout; int running = 1;
int noPorts; int port;
unsigned short portNo;
/* Socket descriptors for server */
/* Maximum socket descriptor value */
/* Set of socket descriptors for select() */
/* Timeout value given on command-line */
/* Timeout for select() */
/* 1 if server should be running; 0 otherwise */
/* Number of port specified on command-line */
/* Looping variable for ports */
/* Actual port number */
if (argc < 3) { /* Test for correct number of arguments */ fprintf(stderr, "Usage: %s <Timeout (secs.)> <Port 1> ...\n", argv[0]); exit(1);
}
timeout = atol(argv[1]); noPorts = argc - 2;
/* First arg: Timeout */
/* Number of ports is argument count minus 2 */
servSock = (int *) malloc(noPorts * sizeof(int)); /* Allocate list of sockets for incoming connections */ maxDescriptor = -1; /* Initialize maxDescriptor for use by select() */
for (port = 0; port < noPorts; port++) { portNo = atoi(argv[port + 2]);
/* Create list of ports and sockets to handle ports */
/* Add port to port list. Skip first two arguments */
servSock[port] = CreateTCPServerSocket(portNo); /* Create port socket */
if (servSock[port] > maxDescriptor) /* Determine if new descriptor is the largest */ maxDescriptor = servSock[port];
}
...

## Slide 91: Multiplexing - Example: echo using stream socket
printf("Starting server: Hit return to shutdown\n"); while (running) {
/* Zero socket descriptor vector and set for server sockets */
/* This must be reset every time select() is called */ FD_ZERO(&sockSet);
FD_SET(STDIN_FILENO, &sockSet); /* Add keyboard to descriptor vector */ for (port = 0; port < noPorts; port++) FD_SET(servSock[port], &sockSet);
/* Timeout specification */
/* This must be reset every time select() is called */ selTimeout.tv_sec = timeout; /* timeout (secs.) */ selTimeout.tv_usec = 0; /* 0 microseconds */
/* Suspend program until descriptor is ready or timeout */
if (select(maxDescriptor + 1, &sockSet, NULL, NULL, &selTimeout) == 0) printf("No echo requests for %ld secs...Server still alive\n", timeout);
else {
if (FD_ISSET(0, &sockSet)) { /* Check keyboard */ printf("Shutting down server\n");
getchar(); running = 0;
}
for (port = 0; port < noPorts; port++)
if (FD_ISSET(servSock[port], &sockSet)) { printf("Request on port %d: ", port); HandleTCPClient(AcceptTCPConnection(servSock[port]));
}
}
}
for (port = 0; port < noPorts; port++) close(servSock[port]); /* Close sockets */ free(servSock); /* Free list of sockets */
exit(0);
}
91

## Slide 92: Multiple Recipients
92
So far, all sockets have dealt with unicast communication
  i.e., an one-to-one communication, where one copy (“uni”) of the data is sent (“cast”)
what if we want to send data to multiple recipients?
1st Solution: unicast a copy of the data to each recipient
 inefficient, e.g.,
consider we are connected to the internet through a 3Mbps line
a video server sends 1-Mbps streams
then, server can support only three clients simultaneously
2nd Solution: using network support
  broadcast, all the hosts of the network receive the message
  multicast, a message is sent to some subset of the host
for IP: only UDP sockets are allowed to broadcast and multicast

## Slide 93: Multiple Recipients - Broadcast
93
Only the IP address changes
Local broadcast: to address 255.255.255.255
  send the message to every host on the same broadcast network
  not forwarded by the routers
Directed broadcast:
  for network identifier 169.125 (i.e., with subnet mask 255.255.0.0)
  the directed broadcast address is 169.125.255.255
No network-wide broadcast address is available
  why?
 In order to use broadcast the options of socket must change:
int broadcastPermission = 1;
setsockopt(sock, SOL_SOCKET, SO_BROADCAST, (void*) &broadcastPermission, sizeof(broadcastPermission));

## Slide 94: Multiple Recipients - Multicast
94
Using class D addresses
  range from 224.0.0.0 to 239.255.255.255
hosts send multicast requests for specific addresses
a multicast group is formed
 we need to set TTL (time-to-live), to limit the number of hops
- using sockopt()
 no need to change the options of socket

## Slide 95: Useful Functions
95
int atoi(const char *nptr);
  converts the initial portion of the string pointed to by nptr to int
int inet_aton(const char *cp, struct in_addr *inp);
  converts the Internet host address cp from the IPv4 numbers-and- dots notation into binary form (in network byte order)
  stores it in the structure that inp points to.
  it returns nonzero if the address is valid, and 0 if not
char *inet_ntoa(struct in_addr in);
  converts the Internet host address in, given in network byte order, to a string in IPv4 dotted-decimal notation
typedef uint32_t in_addr_t;
struct in_addr { in_addr_t s_addr;
};

## Slide 96: Useful Functions
96
int getpeername(int sockfd, struct sockaddr *addr, socklen_t *addrlen);
  returns the address (IP and port) of the peer connected to the socket
sockfd, in the buffer pointed to by addr
  0 is returned on success; -1 otherwise
int getsockname(int sockfd, struct sockaddr *addr, socklen_t *addrlen);
  returns the current address to which the socket sockfd is bound, in the buffer pointed to by addr
  0 is returned on success; -1 otherwise

## Slide 97: Domain Name Service
struct hostent *gethostbyname(const char *name);
  returns a structure of type hostent for the given host name
  name is a hostname, or an IPv4 address in standard dot notation
e.g.
gethostbyname(“www.csd.uoc.gr”);
struct hostent *gethostbyaddr(const void *addr, socklen_t len, int type);
  returns a structure of type hostent for the given host address addr of length len and address type type
struct hostent {
97
char | *h_name; | /* official name of host */
char | **h_aliases; | /* alias list (strings) */
int | h_addrtype; | /* host address type (AF_INET) */
int | h_length; | /* length of address */
char | **h_addr_list; | /* list of addresses (binary in network byte order) */
}
#define h_addr h_addr_list[0] /* for backward compatibility */

## Slide 98: Domain Name Service
struct servent *getservbyname(const char *name, const char *proto);
  returns a servent structure for the entry from the database that matches the service name using protocol proto.
  if proto is NULL, any protocol will be matched.
e.g. getservbyname(“echo”, “tcp”) ;
struct servent *getservbyport(int port, const char
*proto);
  returns a servent structure for the entry from the database that matches the service name using port port
struct servent { char *s_name;
98
char **s_aliases;
int s_port; char *s_proto;
/* official service name */
/* list of alternate names (strings)*/
/* service port number */
/* protocol to use (“tcp” or “udp”)*/
}

## Slide 99: Compiling and Executing
99
include the required header files
Example:
milo:~/CS556/sockets> gcc -o TCPEchoServer TCPEchoServer.c DieWithError.c HandleTCPClient.c milo:~/CS556/sockets> gcc -o TCPEchoClient TCPEchoClient.c DieWithError.c milo:~/CS556/sockets> TCPEchoServer 3451 &
[1] 6273
milo:~/CS556/sockets> TCPEchoClient 0.0.0.0 hello! 3451
Handling client 127.0.0.1
Received: hello! milo:~/CS556/sockets> ps
PID TTY
5128 pts/9
6273 pts/9
6279 pts/9
TIME CMD
00:00:00 tcsh
00:00:00 TCPEchoServer
00:00:00 ps
milo:~/CS556/sockets> kill 6273 milo:~/CS556/sockets>
[1] Terminated milo:~/CS556/sockets>
TCPEchoServer 3451

## Slide 100: The End - Questions
100